## Slide 1
8. Spectral Calibration
Dr. David R. Thompson
Jet Propulsion Laboratory, Imaging Spectroscopy Group

## Slide 2
Goals for this module
Resample spectra using spectral response functions
Recognize and correct spectral calibration errors

## Slide 3: Conventions
Samples (cross-track locations)
Rows (spectral channels)
Spectrometer
Telescope
FPA
Slit
Recall our idealized Focal Plane Array (FPA).
Spectral Calibration is the process of determining the wavelengths to which each FPA row responds.
Each detector element is sensitive to a range of wavelengths.

## Slide 4: Flavors of non-uniformity
courtesy
Robert O. Green, JPL
Wavelength
Cross Track Sample
Requirement
Failure by Frown
Failure by Twist
Failure by Spectral-IFOV-Shift
Wavelength
Physical detectors often exhibit different kinds of alignment-related nonuniformities.
These distortions should also be characterized during the spectral calibration process.

## Slide 5: Uniformity achieved
(courtesy Robert O. Green, JPL, and others)
Hyperion 2000
CRISM 2005
JPL M3 2008
AVIRIS-NG
[Thompson et al., AMT 2015]

## Slide 6: Spectral response functions
Typically we assume detector elements have Gaussian responses with known Full Widths at Half Maximum (2.355 standard deviations).
To simulate a channel’s measurement of a high-resolution feature, we sum all wavelengths, weighting by the relative response of the channel. Make sure the response function itself integrates to unity!

## Slide 7: Wavelength fitting
Courtesy Robert O. Green
Often the best spectral calibration standard is the atmosphere itself. By fitting the measurement (green) to the known features of the atmosphere (red) we find the best-matching wavelength spacing and offset.

## Slide 8: Wavelength fitting with the atmosphere
Solar zenith
1. Calculate an average Top of Atmosphere (TOA) reflectance for each cross-track position. This normalizes for the variable solar illumination, expressing the measurement as a fraction of incoming irradiance.
Measured radiance
Solar irradiance
Typical TOA reflectance values are greater than zero, and less than one.

## Slide 9: Wavelength fitting (contd.)
2. Get a transmission spectrum for an obvious, sharp atmospheric feature using an appropriate Radiative Transfer Model (I often use 6s or MODTRAN).

## Slide 10: Wavelength fitting (contd.)
We model the observation as a linear “continuum” multiplied by the transmittance and then sampled by the instrument
Continuum
Continuum x Transmittance
Measurement

## Slide 11: Wavelength fitting (contd.)
Position of linear continuum
3. Use a nonlinear optimization routine to fit continuum and absorption depth. We find the model which best fits the measured feature (note – this only works over short wavelength intervals
Spectral response
Absorption shift, depth

## Slide 12: Wavelength fitting example
Apparent reflectance
Residual error
Apparent reflectance
Residual error
Common features used for this purpose include the oxygen A band (760 nm) and Near-Infrared H2O vapor absorptions
[Thompson et al., Atmos. Meas. Techniques 2015]

## Slide 14: Exercise 8: Spectral Calibration
Objective: Use the atmosphere as a calibration object. Fit a modeled transmission spectrum to TOA observations.
Files include two examples of TOA reflectances acquired by the AVIRIS-NG instrument onboard a b-200 aircraft over Ivanplah playa. The exercise notebook contains fitting routines, and a transmission spectrum for appropriate observing geometry and water vapor loadings.
Pick an atmospheric feature, and eyeball an initial calibration. Start with a spectral response function that is 5-6 nm Full Width at Half Maximum. Then, fit wavelength shifts to fine tune your initial guess. Is there a way of quantifying how accurate this method can be?