## Slide 1
11. Optimal Estimation: Theory and Practice
Dr. David R. Thompson
Jet Propulsion Laboratory, Imaging Spectroscopy Group

## Slide 2
Goals for this module
Apply OE to fit combined surface and atmosphere models
Construct new prior distributions
Correctly balance instrument and prior information

## Slide 3: Orbital spectroscopy will necessitate improved atmospheric correction
Traditional atmospheric correction methods have trouble in certain conditions:
High water vapor
Extreme viewing angles
Surface/atmosphere coupling
Heavy aerosol loads
Orbital missions will access tropical and subtropical environments that:
Host a large fraction of Earth’s productivity and biodiversity
Are underrepresented in atmospheric correction research
Often have “difficult” atmospheres
Most current aerosol retrieval methods use dark or shadowed pixels that may not be apparent at orbital ground sampling resolutions
Existing methods generally disregard uncertainties

## Slide 4: Optimal Estimation (OE) Theory: Simultaneous estimation of surface and atmosphere
OE is one of a family of Bayesian model inversion approaches, and particularly common in remote sensing literature. Popularized by Clive Rodgers, [2000]
The basic idea is to create a comprehensive model of the surface/atmosphere system and fit all free parameters simultaneously.
It is a true spectroscopic retrieval that can exploit information distributed across the spectrum, helping to disentangle surface and atmosphere.
Other advantages include:
Comprehensive uncertainty estimates to inform downstream analyses
Flexible state vectors, more robust for difficult observing conditions
Elegance, conceptual simplicity
Notes: Traditional atmospheric correction typically: (!) LUT generation of coefficients, (2) estimate of atmospheric state, (3) algebraic correction based on lambertian assumptions. Mature and effective; form basis of methods used in AVIRIS-NG standard products.
Several challenges to this…
limited size of state vector
Algebraic approximate solutions less accurate for extreme geometries
Uncoupled
Algebraic inversion means difficult to tease apart smooth atmospheric effects
Most inaccurate in regions of high haze, extreme water vapor causing absorption in scattering. India dataset contains pushes the frontier, excelelnt opportunity for investigating next level of precision.
Enabled by a fast radiative transfer model as an interior loop of an iterative max. a posteriori estimation

## Slide 5: The “forward problem”
5
State vector
Measurement
Forward model
The forward problem involves predicting the measurement from some atmospheric and surface state. We already know how to do this pretty well.

## Slide 6: The “inverse problem”
6
Estimated state vector
Measurement
Inversion algorithm
The inversion starts from a measurement and infers the most probable state. This is tougher because (a) there may be more unknowns than measurements, and (b) there is often instrument noise in the measurement.

## Slide 7: Maximum A Posteriori solution
Taking the logarithm of p(x | y), and ignoring terms that are constant with x, reduces the Maximum A Posteriori problem to the optimization:
… we can solve it by conjugate gradient descent.
Bayesian prior
Model match to measurement
Cost

## Slide 8: Reprise: “Classic” atmospheric correction is a sequential procedure
Lookup table indexed by H2O, etc.
1. In advance, do RTM calculations for a grid of atmospheric conditions:
TOA reflectance
Surface reflectance
4. Algebraic Inversion
2. Analyze radiance to estimate this atmosphere (typically using band ratios).
Path reflectance of atmosphere
Spherical sky albedo
Upward/downward transmission along optical path for known geometry
3. Look up and/or interpolate optical coefficients
Notes: With atmospheric state specified, We can get optical constants via linear lookup table interpolation (note: T=transmission, S=spherical sky albedo, rho_a is the path reflectance).
This is just one of several similar functional approximations to the actual radiative transfer solution. With atmosphere specified, we can invert it algebraically to recover the surface reflectance.
The conventional strategy is limited in sever

## Slide 9: OE involves iterative, simultaneous estimation of atmosphere and surface
Bayesian prior
Model match to measurement
Cost
1. Predict radiance
2. Optimize state vector

## Slide 10: Pictoral representation
xATMOS
xSURFACE
Iterative optimization is like “hill climbing” of the probability, starting from our initial guess of the surface/atmosphere state. We can calculate a local linearized Gaussian error estimate (the ellipsoid) at the solution.

## Slide 11: The Jacobian matrix
Consider the first order Taylor series expansion:
A local approximation, which is exact for linear problems
Elements of :
The Jacobian is an important part of the optimization, and it tells us a lot about our sensitivities to different state vector elements. It represents the state parameters’ influence on the observation.

## Slide 12: The Jacobian matrix
A more compact form is simply:
It can be written explicitly as:
where

## Slide 13: The Jacobian matrix
A single reflectance value
Atmospheric H2O column

## Slide 14: Posterior predictive uncertainty
xATMOS
xSURFACE
Our predictive uncertainty at the solution is a multivariate Gaussian distribution incorporating both prior and measurement noise.

## Slide 15: The observation noise
Total observation noise
Measurement noise (instrument effects)
Photon noise
Read noise
Dark current noise
Unknown parameters in the observation system
Sky view factor
H2O absorption coefficient intensity
Systematic radiative transfer error
Uncorrelated radiative transfer error
Jacobian WRT unknowns
The observation noise term is very flexible. It typically incorporates both instrument noise as well as unknowns in the observation system that are not retrieved.

## Slide 16: Components of the Forward Model (example)
Retrieved in the inversion
Instrument: AVIRIS-NG
Instrument model with Wavelength- and signal-dependent SNR
Photon shot & read noise
Uncorrelated calibration uncertainty
Systematic calibration / RT uncertainty
Atmosphere: MODTRAN 6.0 RTM
Rural aerosol model
Midlatitude summer profile
H2O, AOD retrieved
Surface: Multi-component Multivariate Gaussians
Reflectance estimated independently in every channel

## Slide 17: Example of multi-component surface models
[Thompson et al., Remote Sensing of Environment 216, 2018]
We will often use multiple multivariate Gaussian priors. During initialization we select one appropriate for the surface type. More information in future presentations…

## Slide 18: Reflectance estimate vs. in situ
Wavelength (nm)
Wavelength (nm)
Comparisons against surface measurements demonstrate accurate retrievals
[Thompson et al., Remote Sensing of Environment 216, 2018]
Notes: Good agreement!

## Slide 19: Aerosol fitting results
Aerosol distortion
Aerosol-related H2O vapor distortions
H2O vapor distortions
Original method
New approach
Simultaneous estimation of surface and atmosphere parameters can account for aerosol distortions
We retrieve three optical types (best interpreted as structured error terms rather than physical particle properties)
Validation on a large segment of the AVIRIS-NG campaign in India, which experienced high water vapor and AOD loadings
AOD550 estimates for AVIRIS-NG India campaign
Original
OE solution
Aerosol type
fractions
Aerosol type
fractions
[Thompson et al., Remote Sensing of Environment, 232, 2019].

## Slide 20: Modeling assumptions affect the relative weighting of measurement and prior
Wavelength (nm)
[Thompson et al., Remote Sensing of Environment 216, 2018]
Instrument noise and calibration uncertainty cause the retrieval to rely more on the prior, and less on the instrument measurement. In this example, the retrieval becomes “smoother” as we increase the presumed calibration error.

## Slide 21: Coastal environments
[Thompson et al., Remote Sensing of Environment 216, 2018]
Wavelength (nm)
Wavelength (nm)
Experiments demonstrate that the same method works for clear and turbid water.
Notes: Posterior uncertainty predictions (grey envelopes) accurately predict and capture our actual discrepancies!
This demonstrates a closed account of the uncertainty in the system. To our knowledge, this is the first time it has been done for VSWIR imaging spectroscopy.
Note: we also account for the uncertainty in the surface measurement, which is a significant contributor to the confidence bands.

## Slide 22: Example: Volcanic AOD observations
AVIRIS-C f170127t01p00r16
(subset, visible bands)
Aerosol Optical Depth at 550 nm
Aerosol Optical Depth Uncertainty
Hot crater
[Realmuto, Thompson, et al., in preparation]
Combined estimate of H2O vapor, AOT, surface reflectance and temperature
Applying the retrieval to an entire image allows pixelwise AOD mapping, as in this example of a volcanic plume.